## Slide 1
GHG Inventory and Net-Zero Roadmap for an SME Textile Manufacturer
Portfolio case study · Harshita Sadhna
Based on a project for a Canadian manufacturer through an SME climate clinic. The company is renamed "Northline Knitwear" and all figures are fictional; methods and assumptions reflect the original work.

## Slide 2
The brief
Client
Mid-sized knitting mill, ~35 staff, one site in boundary. Sources yarn from India, China and the US and ships to Canada and the US.
Ask
Build a first credible GHG inventory and a practical path to net zero the owners could act on.
My role
Two-person team. I built the calculation model, defined boundaries and assumptions, and drafted the reduction roadmap.

## Slide 3
Value chain and what we measured
Operational control approach under the GHG Protocol Corporate Standard
Yarn and fabric production
Scope 3 · Cat 1
Sea, rail and truck to facility
Scope 3 · Cat 4
Knitting facility: gas, electricity, vehicles
Scopes 1 and 2
Truck to customers
Scope 3 · Cat 9
Also included
Employee commuting (Cat 7), by mode
Business travel flights (Cat 6)
Out of boundary for now
Dyeing and finishing site (separate operator)
Waste, product use and end-of-life (Cats 5, 11, 12)

## Slide 4
From spend-based to activity-based
The first pass used dollars spent; the final model uses physical quantities wherever data allowed
First pass: spend-based
$ spent on yarn and freight x industry-average factors
No split by fibre or sourcing country
Commuting and travel left out
Easy to run, but hides where emissions come from
Final model: activity-based
kg of yarn by fibre and country x LCA factors
Freight in tonne-km by sea, rail and truck
Commuting and business travel added
Several times higher, and shows the hotspots

## Slide 5
How each number is built
×
Activity data
kg, kWh, m³, tonne-km, passenger-km
=
Emission factor
tCO₂e per unit, from ECCC, US EPA and LCA studies
Emissions
tCO₂e by scope and category
Data sources
Monthly gas and electricity bills · yarn and fabric purchase volumes · freight routes and ports · employee commute survey · flight records. Where data was missing, each gap was filled with a stated assumption so the client could replace it later.

## Slide 6
Results: Scope 3 is almost the whole footprint
7,870
tCO₂e total
77
Scope 1
20
Scope 2
98.8%
in Scope 3
What this means for the client
Owned operations are small; Ontario’s low-carbon grid keeps Scope 2 near zero.
Real reductions depend on what yarn is bought and from where, not on factory energy.
Supplier data is the single biggest lever for accuracy and for cutting emissions.

## Slide 7
Purchased materials dominate Scope 3
Scope 3 by category, tCO₂e
Chart: 
| Polyester yarn | Polyester fabric | Cotton yarn | Upstream transport | Downstream transport | Employee commuting | Business travel
tCO2e | 2856 | 2570 | 2088 | 166 | 69 | 19 | 5
Takeaways
Yarn and fabric are 95% of Scope 3.
Polyester carries nearly twice the factor of cotton per kg.
Freight matters less than expected once measured in tonne-km.

## Slide 8
Where yarn comes from changes its footprint
Yarn emissions by sourcing country, tCO₂e
Chart: 
| India | China | US
Cotton | 1073 | 717 | 298
Polyester | 1428 | 1000 | 428
India
Lower cotton yields mean more land, water and fertilizer per kg. Priority for supplier engagement.
China
Higher yields but heavy irrigation and fertilizer. Work with suppliers on inputs.
US
Mechanized, largely rain-fed farming. Lowest factor; shift share here where feasible.

## Slide 9
Assumptions made explicit
Every data gap was documented so the estimate can be audited and improved
Sourcing
Volumes split by country and fibre from purchase totals; poly-cotton blends split into fibre shares
Ports and routes
Nearest major export hub per country; sea to West Coast, then rail and truck
Freight loads
15,000 kg per truck to estimate trips; heavy-duty truck factor where fuel data was missing
Customers
Delivery addresses unknown, so regional average distances applied
Fleet
No fuel logs, so a share of freight spend used as a spend-based proxy
Travel
All flights treated as medium-haul, one passenger each; hotels excluded

## Slide 10
What the client should collect next year
1
Purchasing
kg of yarn per country and fibre; recycled content share
2
Inbound freight
Port of origin, shipments per route, carrier fuel or km reports
3
Outbound freight
Customer city, shipments per customer, weight per trip
4
Travel
Departure and arrival airports, passengers per trip
5
New categories
Waste by type, dyeing-site energy use, product disposal split

## Slide 11
Reduction levers, ranked by impact
Materials
Highest impact
Shift polyester to recycled PET
Source low-carbon cotton
Engage top suppliers on energy and fertilizer
Logistics
Medium
Consolidate shipments
Use carriers with low-emission fleets
Nearshore where feasible
Operations
Lower, but direct control
Heat pumps as gas equipment retires
Electric forklifts and vehicles
Energy management and LED retrofits

## Slide 12
A phased path to net zero by 2050
2025–28
~10–15%
Track real fuel use; energy audit and LEDs; renewable electricity certificates; audit top 10 suppliers
2029–33
~30–35%
Heat pumps at end of life; begin EV fleet; 30–50% recycled polyester; consolidated freight
2034–42
~60–70%
Full heat pump rollout; 70%+ low-carbon yarn; nearshore key sourcing; virtual-first travel
2043–50
Net zero
Fully electric site on renewables; decarbonized logistics partners; remove residual 5–10% with verified removals

## Slide 13
What this project shows
GHG Protocol boundary setting and Scope 1, 2 and 3 accounting for an SME
Turning incomplete client data into a documented, auditable estimate
Translating results into a roadmap a small business can act on
Company name and all figures are fictional. Original client data is confidential.